## Slide 1: Lights. Camera. Paper.
How to take a boring photograph
Benjy Marks

## Slide 2: So you have an experiment

## Slide 3: And you see something

## Slide 4: Now what?
Observation
Paper
?

## Slide 5: Step 1: Set the scene
Black/white backdrop
If you’ll be there a while, get rid of natural light
Vibrations
Data storage
Tripod + quick release + levels

## Slide 6: Tripods
(7dslr.com)

## Slide 7: Step 2: Lighting
(wikimedia.org)

## Slide 8: High key lighting
(wikimedia.org)

## Slide 9: Low key lighting
(wikimedia.org)

## Slide 10: Point sources
(pssl.com)

## Slide 11: Point lighting
Object
Camera

## Slide 12: Point lighting
Object
Camera

## Slide 13: Diffuse lighting
(aliexpress.com)
(hsreflections.com.au)

## Slide 14: Light boxes
(kmart.com.au)

## Slide 15: Light boxes
(instructables.com)

## Slide 16: Diffuse lighting
Object
Camera
Light box
Light box

## Slide 17: Transmission lighting
Light box
Camera

## Slide 18: Flashes

## Slide 19: Flickering
Normal AC power - 50Hz or 100Hz
Fluorescent lights – 5kHz to 40kHz
DC power – minimal flicker

## Slide 20: Colour Temperature
Planck’s law:
(wikimedia.org)

## Slide 21: Colour Temperature
Planck’s law:
(wikimedia.org)

## Slide 22: Temperature
(wikimedia.org)

## Slide 23: Step 3: Picking a camera
(digital-photography-products.com)

## Slide 24: Wavelength
(astrosurf.com)

## Slide 25: Sensors
(digitalbolex.com)

## Slide 26: Sensors
CCD
Converts light to electrons
Global shutter
Charge read on all pixels simultaneously
High quality, low noise
Most photons hit sensor
Use lots of power
Expensive to produce
CMOS
Converts light to electrons
Rolling shutter
Charge read pixel by pixel
More susceptible to noise
Many photons miss sensor
Low power consumption
Cheap to produce

## Slide 27: Rolling or global shutters
(andor.com)

## Slide 28: Optical cameras
(kenrockwell.com)
(nikonusa.com)

## Slide 29: The DSLR
(digit.in)

## Slide 30: Single lens reflex cameras
(wikimedia.org)
Front-mount lens
Reflex mirror
Focal plane shutter
Film or sensor
Focusing screen
Condenser lens
Optical glass pentaprism
Eyepice

## Slide 31: Setting 1: ISO
International Organisation for Standardisation
  IOS in english
  OIN in french
Thought to refer to the greek ‘isos’ (equal)
Proof of the futility of committees

## Slide 32: ISO
Refers to light sensitivity
Not one but five independent ways to measure ISO. All subjective.
Can be set manually or automatically
Higher ISO means more sensitive to light
Generally this means less light must be accumulated, and the image becomes ‘grainier’.

## Slide 33: ISO
(International Organisation for Standardisation)
(elliezenhari.com)

## Slide 34: Setting 2: Focal length
(nikonusa.com)

## Slide 35: Focal length
(nikonusa.com)

## Slide 36: Setting 3: F-stop
(vagabond3.com)

## Slide 37: The pinhole effect
(wikimedia.org)

## Slide 38: F-stop and depth of field
(simoneskitchen.net)

## Slide 39: Setting 4: Shutter speed
(sharinakagawaphotography.wordpress.com)

## Slide 40: Setting 5: White balance
(learntouseacamera.com)

## Slide 41: Setting 6: Frame rate
(photohead.com)

## Slide 42: Typical frame rates
Still photos
DSLRs: up to 7 fps
MILCs: up to 20 fps
Video
DSLRs: up to 60 fps
MILCs: up to 1200 fps

## Slide 43: Sensor size
(wikimedia.org)

## Slide 44: Step 4: Picking a lens
(wikimedia.org)

## Slide 45: Picking a lens: Mounts
Canon
  DSLRs take EF mounts
  Mirrorless take EF-M (usually)
Nikon
  DSLRs take F-mount
  Mirrorless take NIKKOR VR
AF/MF

## Slide 46: Picking a lens: Focal length
Prime lens – no zoom!
Macro lens
Fish eye
Wide angle
Standard
Portrait
Telephoto
Super Telephoto

## Slide 47: Picking a lens: distortion
(photographylife.com)

## Slide 48: Picking a lens: the complexity
Sensor size |  | 35 mm or full-frame | APS-H | APS-C | Four Thirds
Crop factor |  | 1.0 | 1.3 | 1.5 or 1.6 | 2.0
Lens view | Angle diag (deg) | Focal length (mm) |  |  | 
Ultra wide-angle | 118 | 13 | 10 | 8 | 7
Typical wide-angle | 84 | 24 | 18 | 15 | 12
 | 75 | 28 | 22 | 18 | 14
Slightly wide-angle | 63 | 35 | 27 | 23 | 18
“Normal” | 59-47 | 40-50 | 30-38 | 25-32 | 20-25
Portrait lens | 29 | 85 | 65 | 55 | 43
 | 23 | 105 | 81 | 68 | 53
Telephoto | 18 | 145 | 104 | 87 | 68
Long telephoto | 8 | 300 | 231 | 192 | 150
Very long telephoto | 2 | 1200 | 923 | 774 | 600

## Slide 49: Shutter release
Push the button
Wired connector
Wireless connector
Smartphone
Tethered to a computer
Simultaneous images?
Using a flash?

## Slide 50: Putting it all together
Find the right lens
Choose a low ISO
Small focal range = low f-stop
Appropriate shutter speed
Keep adding lights
Take an image or a time lapse

## Slide 51: Image formats
RAW
Tiff
Jpeg
Png

## Slide 52: RAW
Essentially a list of pixel voltages
Needs more information
Huge files

## Slide 53: Tiff
Tagged image file format
(Can have) lossless image compression
Big files
Good to use

## Slide 54: Jpeg
Joint Photographic Expert Group
Flexible lossy compression options
Small files
OK to use

## Slide 55: Png
Portable Network Graphics
(Can have) lossless image compression
Supports 8-bit transparency
Only RGB
Not for us

## Slide 56: Video formats
RAW video
Mjpeg
Mp4
Avi
MOV
Generally the camera will only give you one option, so use that!

## Slide 57: RAW video
Direct sensor output
Needs calibration curves
Massive files
Great for post-processing, but not for us

## Slide 58: Interlaced and progressive

## Slide 59: SD Cards
Space:
  SD: 128MB to 2GB
  SDHC: 4GB to 32GB
  SDXC: 64GB to 2TB
Speed:
  Class 2: 2 MB/s
  …
  Class 10: 10MB/s
  UHS-I: 50-100 MB/s
  UHS-II: 150-300 MB/s

## Slide 60: Storage
(digitalcameraworld.com)

## Slide 61: Tethering
Windows: Camera Control Pro (paid)
Mac: Remote Camera Control (free)
Linux: gphoto2 (open source)
+ many, many others….
Live view on Mac/Windows only! (at least for Nikon)

## Slide 62: Common conversions
Command line tools:
  Any OS: ffmpeg
  Mac OSX: image magick
Graphical tools:
  Any OS: ImageJ (Fiji)
  Any OS: GIMP
  Complicated: Photoshop

## Slide 63: Between image types
Convert NEF to JPG:
ufraw-batch *.nef --out-type=jpeg
Rotate an image:
convert *.jpg -rotate 180 1%04d.jpg

## Slide 64: Image to video
Convert JPG to mp4:
avconv -f image2 -i *.jpg -r 20 foo.mp4

## Slide 65: Video to image
Convert movie to jpg:
avconv -i foo.mov -vsync 1 -r 25 -an -y -qscale 1 out_%04d.jpg
OR
ffmpeg -i video.mpg image%d.jpg

## Slide 66: Loading up images
Matlab:
  imread(filename);
Python:
  np.imread(filename)
  cv2.imread(filename)
  PIL.Image.open(filename)
ImageJ (Fiji):
  File -> Open